## Slide 1: Upgrade Firmware
Through J-Link

## Slide 2: Step 1
Download Segger Softwae Package v6.60B https://www.segger.com/downloads/jlink/

## Slide 3: Step 2
Connect S76S / S68S / S76G S78G to J-link through SWD interface
  SWCLK/SWDIO/RESET/GND

## Slide 4: Step 3 choose device->choose firmware-> Program Device
Device:STM32L073VZ
Choose firmware file＿

## Slide 5: Step 4
After Firmware Update
  Please run
    sip factory_reset
    mac save
    sip reset